## Slide 1: Investigating Process Behaviour Using Functional Data Analysis
Jim McLellan
Department of Chemical Engineering
Queen’s University
Kingston, ON
Canada
james.mclellan@chee.queensu.ca

## Slide 2: Functional Data Analysis (FDA)
FDA is an evolving statistical framework in which responses are profiles, not points

## Slide 3: Functional Data Analysis (FDA)
FDA is an evolving statistical framework in which responses are profiles, not points
FDA has potential for making it easier to estimate dynamic and steady-state models for chemical processes

## Slide 4: Functional Data Analysis (FDA)
FDA is an evolving statistical framework in which responses are profiles, not points
FDA has potential for making it easier to estimate dynamic and steady-state models for (chemical) processes
Potential of FDA needs to be assessed. Could FDA help solve your model estimation problems?

## Slide 5: Functional Data Analysis
Motivation
Functional data analysis
2 Stories –
Estimating differential equation models using principal differential analysis
Obtaining reactor settings for desired molecular weight distributions using functional regression

## Slide 6: Motivation
When modeling and controlling chemical processes, we frequently encounter responses that are functional – functions of an independent variable such as time or molecular weight
  time traces (time series) – most frequently encountered in process monitoring and control
  species distributions – e.g., polymer molecular weight distributions, particle size distributions
  spectra
The data object is a function of one or more independent variables.
How do we work with these responses?

## Slide 7: Ways of viewing functional data
Sampled data series
Multiple responses
Functional data objects

## Slide 8: Ways of viewing functional data
Sampled data series
  standard approach for dealing with time traces – time series – predominant approach in control modeling and analysis
  typically assume uniform sampling – measurements are available at regular intervals
  models are typically discrete-time – difference or recursion equations e.g., yk+1 = a1yk + b1uk-1+ek
Multiple responses at discrete points from continuous models
  typical approach in fundamental process modeling – e.g., predicting polymer molecular weight distributions at different chain lengths, chemical concentrations at different times, particle size distributions
  responses are measurements at particular times or positions
Functional data objects
  the data object is a continuous curve

## Slide 9: Goals of this talk
Demonstrate how FDA techniques can be used to model dynamic and steady-state process behaviour
Provide an overview of two relevant FDA techniques
    Principal differential analysis
    Functional regression
Comment on the relationship between FDA approaches and existing approaches

## Slide 10: Functional Data Analysis (FDA)
… is a statistical framework in which the data object is a function of one or more independent variables
  Techniques have been developed and used for analyzing handwriting, lip motion, horse gait data, analyzing weather data, eye-hand response times, …
  Primary reference – Ramsay and Silverman (1997, 2002) – text
  FDA toolbox for Matlab available free from Jim Ramsay web site (www.psych.mcgill.ca/faculty/ramsay.html)
Datasets consist of collections of functional observations
  Multiple observations (realizations) of same response function – e.g., temperature profiles for different runs in a batch reactor – {y1(t), y2(t),…, yN(t)}
  Observations of different functional responses – e.g., time traces for valve input and temperature – {u(t), y(t)}

## Slide 11: Functional Data Analysis (FDA)
FDA is a statistical framework for functional data
  Standard summary measures defined - examples
    Sample average
    Sample variance
    Sample covariance, sample cross-covariance, sample covariance matrix
Note that the result is a function of the independent variable – average function, variance function.

## Slide 12: Functional Data Analysis
Concept
  data objects are continuous functions of an independent variable
Practice
  observations are typically taken at discrete intervals – not necessarily uniform – and functional observations are constructed using appropriate basis functions - smoothing
are basis functions e.g., splines, polynomials, sinusoids

## Slide 13: Two Stories about Functional Data Analysis
Story #1 – Estimating parameters in differential equation models using Principal Differential Analysis (PDA)
  M.Sc. student Andy Poyton, Ph.D student Saeed Varziri
  Collaboration with Kim McAuley, Jim Ramsay
Story #2 – Obtaining reactor settings for desired molecular weight distributions using Functional Regression
  Collaboration with Robin Hutchinson, Hana Sulieman

## Slide 14: What is Principal Differential Analysis (PDA) and Why are We Using it?
PDA is a technique from Functional Data Analysis (FDA)
PDA exploits natural smoothness of processes
  enables analysis using derivatives and rate behaviour
Does PDA have potential for estimating parameters in dynamic models?
  yes

## Slide 15: Estimating Differential Equation Models Using Principal Differential Analysis (PDA)
Parameter estimation in fundamental dynamic models is difficult and iterative using traditional techniques
Most computational effort arises from repeated numerical solution of ODEs

## Slide 16: Estimating Differential Equation Models Using Principal Differential Analysis (PDA)
Parameter estimation in fundamental dynamic models is difficult and iterative using traditional techniques
Most computational effort arises from repeated numerical solution of ODEs
Principal Differential Analysis (PDA)
  Uses smoothing of dynamic data to provide time derivatives
  Converts ODE estimation to an algebraic problem
  Eliminates need to solve dynamic equations numerically
  Estimates parameters so that differential equation models are satisfied by observed functional responses

## Slide 17: Smoothing
The first step in any functional data analysis is to obtain a functional representation of the data
  Discrete data are represented as a function of time using basis functions, rather than as a collection of discrete set of points
Smoothing using basis functions

## Slide 18: Smoothing
The first step in any functional data analysis is to obtain a functional representation of the data
  Discrete data are represented as a function of time using basis functions, rather than as a collection of discrete set of points
  Functional data are a set of curves with one pair of curves for each run
  Functional data objects are linear combinations of known basis functions (e.g., B-splines)
Smoothing using basis functions

## Slide 19: Smoothing
The first step in any functional data analysis is to obtain a functional representation of the data
  Discrete data are represented as a function of time using basis functions, rather than as a collection of discrete set of points
  Functional data are a set of curves with one pair of curves for each run
  Functional data objects are linear combinations of known basis functions (e.g., B-splines)
Smoothing using basis functions

## Slide 20: Principal Differential Analysis
Assess model fit by how well and satisfy the ODE
  E.g., for substitute in the smoothed curves and their derivatives, and the predicted parameters producing a residual curve
Estimate parameters and to minimize the squared residuals

## Slide 21: PDA Parameter Estimation is a two-step process
Data are smoothed and put in functional form
    ck values are spline coefficients
    Roughness penalties on higher-order derivatives of can be used to adjust smoothness
Squared residual curve is minimized to obtain parameter estimates and
  No numerical solution of the ODE is required. Differentiate to obtain

## Slide 22: PDA Parameter Estimation Example
Linearized CSTR model to produce example with known analytical solution
1 linear ODE, 2 nonlinear parameters to estimate
Generate simulated responses with white noise
Compared PDA estimation with conventional nonlinear least squares estimation
  Computing time
  Precision and bias of parameter estimates
  Precision and bias of model predictions

## Slide 23: Linearized Non-Isothermal CSTR
Linearized model with nonlinear parameter dependence (Marlin, 2000)
  Input – reactor temperature T (perfect T control)
  Constant inlet concentration and flow
  Parameters are k0 and E/R . True values are k0 = 1.0 x 1010 min-1, and E/R = 8330.1 K
CA
F
T
TC

## Slide 24: Linearized Non-Isothermal CSTR
Linearized model with nonlinear parameter dependence (Marlin, 2000)
  Input – reactor temperature T (perfect T control)
  Constant inlet concentration and flow
  Parameters are k0 and E/R . True values are k0 = 1.0 x 1010 min-1, and E/R = 8330.1 K
CA
F
T
TC
 | k0/1010 (min-1) | E/R/103 (K)
PDA | 1.591 | 8.580
NLS | 0.997 | 8.329
True | 1.000 | 8.330
First PDA Attempt
Not so good!

## Slide 25: What was wrong?
  Poor spline fit to data
  Cubic B-spline requires first and second-order derivatives to match at intersection of adjacent intervals
  Can’t match sharp corner – problem for all first-order models with step inputs
Sharp corners cannot be captured by spline

## Slide 26: Fixing the spline fit: knot placement
Cubic B-splines require continuous 1st and 2nd derivatives at knots, giving poor fits near sharp corners
Multiple knots at or near sharp corners (3 for cubic B-splines) alleviate this problem and give better spline fit
put more knots here?
Examined effects of
Coincident knots at sharp corners
Closely spaced (not coincident) knots near sharp corners
Improved spline fits on parameter estimates in ODE model

## Slide 27: Results of PDA with Coincident Knots
Simulations – step down in T; 30 runs simulated
Base case: cubic B-splines with uniform knot spacing at 0.1 min intervals
Spline smoothing was much improved using coincident knots
Parameter estimates and model predictions were as good as those obtained using conventional nonlinear least squares
PDA with coincident knots required less runtime
Adding coincident knots was significantly more effective than adding closely-spaced knots
 | k0/1010 (min-1) | E/R/103 (K) | Run time (sec)
Original PDA | 1.591 | 8.580 | 0.219
PDA w/ coincident knots | 0.998 | 8.329 | 0.219
PDA w/ close knots | 1.216 | 8.438 | 0.234
Traditional NLS | 0.997 | 8.329 | 0.750
True Parameter Values | 1.000 | 8.330 | -

## Slide 28: Smoothing and PDA
The smoothing step is critical to the success of the parameter estimates in PDA
Traditional spline-fitting approach is to penalize higher-order derivatives of the smoothed functions
  Produces poor results for responses with sharp corners or oscillations
We can improve the smoothing step by incorporating underlying ODE model structure into the spline fitting
  Use ODE model with parameter guesses to define roughness penalty for spline smoothing
iteratively re-weighted PDA

## Slide 29: Iteratively re-weighted PDA (iPDA)
Profile-based PDA objective function for fitting splines
Find spline coefficients that minimize
Residuals between spline fit and data points
Ensure spline matches data
“Shrink” spline fit to agree with mechanistic model
where

## Slide 30: Profile-Based PDA – Use the ODE to Help Spline Fitting
Conventional PDA is a 2-step procedure
  Fit splines to data
  Estimate ODE model parameters using fitted splines
Iteratively re-weighted PDA (iPDA) iterates between smoothing and parameter estimation steps
  Fit splines using ODE model (with current parameter estimates) to define a roughness penalty
    Ensures spline fits are smooth and physically reasonable
  Update model parameters using fitted splines
    Adjust ODE parameters to improve ODE model fit to splines
  Iterate between steps 1 and 2 until convergence
Or…
Just solve the combined parameter estimation/spline smoothing problem
  This is the current approach we are using - formulate as an approximate maximum likelihood estimation problem

## Slide 31: PDA Summary
Functional Data Analysis treats data as curves rather than points
Principal Differential Analysis can fit parameters in models without numerical solution of the ODE; effort is in fitting splines to the data - linearized CSTR model with 2 non-linear parameters
iPDA uses ODE as spline-fitting penalty
  can be applied to MIMO ODE models with many parameters
  Example: nonlinear CSTR model with 2 ODEs and 4 nonlinear parameters
Extensions -
  Estimating parameters when some states are unmeasured
  Estimating parameters when there are stochastic disturbances present
  Confidence interval expressions for parameter estimates
  Approximate maximum likelihood formulation

## Slide 32: Two Stories about Functional Data Analysis
Story #1 – Estimating parameters in differential equation models using Principal Differential Analysis (PDA)
Story #2 – Obtaining reactor settings for desired molecular weight distributions using Functional Regression

## Slide 33: Obtaining reactor settings for desired MWDs using Functional Regression
Polymer molecular weight distributions (MWDs) are important because they influence end-use and processing properties
MWDs are functional observations, in which weight fraction is a function of molecular weight (or log(MW))
Conventional approaches for modeling and predicting MWDs include
  characterization using moments
  detailed mechanistic models to predict fractions for each chain length
  discretization and treatment as multi-response estimation problems
Issues
  loss of information vs. complexity
  problem conditioning
Alternative is to treat the MWDs as curves, and use techniques from Functional Data Analysis (FDA)

## Slide 34: Functional Regression
Models in which in which factors or responses are functional
Example – functional response y(r) depends on non-functional factors x1 and x2
  In the MWD modeling example, the response is functional and the factors are non-functional, so parameters in the model are functions of the independent variable r, which is log(MW)

## Slide 35: Functional Regression
Least squares estimation criterion – minimize integral squared error between predicted and observed response functions
Solution – can be determined by expressing parameter functions using basis functions

## Slide 36: Functional Regression for MWD Analysis
Estimate an empirical model to predict the effect of isothermal reactor temperature (T) and initial initiator concentration [I]0 on the resulting MWD for bulk polymerization of styrene in a batch reactor
Response (differential weight fraction, y) is functional, while factors T and [I]0 are non-functional
Synthetic data generated for a 22 factorial design in T and [I]0 using a fundamental model
T
[I]0
-1
1
1
-1

## Slide 37: Functional Regression for MWD Analysis
Steps
  Smooth the raw MWD data using spline basis functions
  Transform MWD responses to ensure model can’t give negative predictions, ensure monotonic behaviour of integral - density function
  Fit main-effects-plus-two-factor-interaction model using transformed responses
    Obtain parameter estimate curves that are functions of log(MW)
  Transform back to original coordinates (differential weight fraction vs. log(MW))
  Use model to determine T and [I]0 to produce MWD near target curve

## Slide 38: Results
  Simulated MWDs are available for 4 combinations of T and [I]0
  Splines gave good fits to the original data plots using 14 basis functions
    4th order B-splines were used with knots at non-uniform intervals
Original data y(r)
Transformed responses
ln(y(r))
Transformed responses
d(ln(y))/dr
computed from spline fits

## Slide 39: Model
0(r) ---- 1(r) ---- 2(r) ---- 12(r) ----

## Slide 40: Model Predictions
Regression model fits simulated data well
Observed (blue) and predicted (red) MWDs
for 22 factorial design
Main-effects-plus-two-factor-interaction model

## Slide 41: Using the model to guide further experimentation
Specified two target distributions, and used model to determine optimal operating conditions
  Conducted as a “blind test” – given target distributions without knowledge of actual operating conditions
  Required operating conditions were correctly identified to within 7% of the true value in both cases
Operating conditions computed to minimize difference between target and predicted MWDs
- solved using Nelder-Mead Simplex algorithm

## Slide 42: What we learned
Influence of Temperature on MWD
  Increasing T reduces average molecular weight
  Increasing T increases the breadth of the MWD
Influence of Initiator on MWD
  Increasing [I]0 reduces average molecular weight
  Increasing [I]0 can produce a shoulder on the MWD – asymmetric influence
Model was useful for selecting operating conditions to produce desired MWDs

## Slide 43: Two Stories about Functional Data Analysis
Story #1 – Estimating parameters in differential equation models using Principal Differential Analysis (PDA)
Story #2 – Obtaining reactor settings for desired molecular weight distributions using Functional Regression

## Slide 44: Functional Data Analysis (FDA)
FDA is an evolving statistical framework in which responses are profiles, not points
FDA has potential for making it easier to estimate dynamic and steady-state models for chemical processes
FDA is useful for both fundamental and empirical models
Potential of FDA needs to be assessed. Could FDA help solve your model estimation problems?
Better understanding is required before FDA will be widely adopted by the chemometrics and chemical engineering community

## Slide 45: Acknowledgements
Research collaborations
  Jim Ramsay, Psychology Dept., McGill
Estimating differential equation models using principal differential analysis
Kim McAuley, Queen’s
Andy Poyton – MSc student, Queen’s
Saeed Varziri – PhD student, Queen’s
Functional regression for modeling MWDs
Robin Hutchinson – Queen’s
  Hana Sulieman – American University of Sharjah, United Arab Emirates

## Slide 46: Acknowledgements
Financial support
Natural Sciences and Engineering Research Council of Canada
MITACS
Queen’s University